## Instruction manual No.11¨

- DIALS AND BUTTONS:

TIME SETTING

1. Pull crown out to position 2. The second minute hand stops moving.

2. Turn crown to advance hour and minute hands.

DATE SETTING

1. Pull crown out to position 1.

2. Turn crown counterclockwise to set date.

* Set the time between 10:00 AM and 09:00 PM, in order for the date to change at night and not during the day.

3. Push crown back to initial position.

USING CHRONOGRAPH

You can track time using chronograph:

1. Press button A once to start/stop chronograph

2. Press button B to reset chronograph. All hands will return to initial position.

RESETTING CHRONOGRAPH (e.g. after battery replacement)

Follow these instructions if the second hand of the chronograph does not return to 00:00 after the reset of the chronograph (e.g. after battery replacement).

1. Pull crown out to position 2.

2. Press button A to set second hand of the chronograph to position 00:00.

3. You can speed up the process by holding buttons A or B.

4. When the second hand is at 00:00, set time and push crown back to initial position.

**Do not push crown back to initial position unless the second hand is at 00:00.

*If you pushed the crown before the second hand reaches 00:00, the second hand would stop and the point at which it stopped would be set as the new initial point (00:00).

# Text boxes

Chronograph: minute hand

Chronograph: second hand

Hour hand

Minute hand

24-hour hand

Crown (3 positions)

Date

Button B

Button A