Instruction manual No.19

Clockwork:

- Date

- Second hand of the watch

- Minute hand of the stopwatch

- Second hand of the stopwatch

Functions of the crown:

K0- Crown in initial position

K1- Position of crown for date setting

K2- Position of crown for time setting

Time setting:

Pull crown out to position K2.  Second hand stops moving. Turn crown clockwise to advance hour and minute hands. Once correct time is set, push crown back to initial position (K0). Second hand starts moving again.

Date setting:

Pull crown out to position K1. Turn crown clockwise to set the date. Once date is set, push crown back to initial position (K0).

Never set the date between 09:00 PM and 04:00 AM. If you do so, the date will change during the day instead of at night.

Using chronograph (stopwatch):

The maximal measurable time is 59 minutes and 59 seconds.

1. Press button A to start/stop the chronograph.

2. Press button B to reset the chronograph.

Buttons A and B will not work during resetting.

Resetting chronograph (e.g. after battery replacement):

Follow these instructions if the second hand of the chronograph does not return to 00:00 after the reset of the chronograph or after battery replacement.

- Pull crown out to position K2.

- Press button A to set second hand of the chronograph to position 00:00. You can speed up the process by holding button A.

- As soon as the second hand is back to its initial position, push crown back to initial position (K0).