(EN) KW9293RF WEATHER station (RC-DCF)

USER MANUAL

1.  Features

1.1	Time			        	-   Radio Controlled Time

-	Perpetual Calendar Up to Year 2099

-	Day of week in 8 languages user selectable

-   Dual Daily Alarm Snooze Function

1.2	Temperature			    -   Indoor measurable range: -9.9~ 50°C

-   Outdoor measurable range: -20 ~ 50°C

-   Outdoor temperature alert function

-   Measures °C / °F user selectable

1.43	Wireless Outdoor Sensor	-	Low-battery indicator for Outdoor Thermo Sensor

-	Wall Mount or Table Stand

-	One Wireless Thermo Sensor Included

-	433MHz RF transmitting frequency

2.  Main Unit Appearance

2.1 Part A- LCD

A1: Time

A2: Radio Controlled Icon

A3: Indoor Temperature/Alarm Time 1

A4: Outdoor Temperature/Alarm Time 2

A5: Projection Time

2.2 Part B- Buttons

B1: “SEARCH “button

B2: “ALERT” button

B3: “Alarm Time 1” button

B4: “MODE” button

B5: “+” button

B6: “RESET” button

B7: “-” button

B8: “ALARM” button

B9: “Alarm Time 2” button

B10: “Projection” button

B11: “SNOOZE/DIMMER” button

2.3 Part C- Structure

C1:Adaptor Plug

3. Outdoor Sensor Appearance.

D1: Transmission Indication LED

D2: Outdoor Temperature

D3: Battery Compartment

D4: Wall Mount Hole

D5: “RESET” button

D6: °C/°F” button

D7: Stand

4. Getting Started:

4.1 Main Unit:

- Connect the power cord to the wall outlet

4.2 Outdoor Thermo Sensor

- Batteries compartment (D3) of thermo sensor is locating behind the back cover,

- Insert 2 x AAA batteries observing polarity [ “+” and “–“ marks]

5. Installation

- Place the main unit to flat surface.

- The remote sensor should be securely mounted onto a horizontal surface.

Note:	Transmissions between receiver and transmitter can reach up to 30m in open area.  Open Area: there are no interfering obstacles such as buildings, trees, vehicles, high voltage lines, etc.

6. Thermometer

6.1 RF Transmission Procedure:

- The main unit automatically starts receiving transmission from outdoor thermo sensor for outdoor temperature after start up.

- The outdoor sensor will automatically transmit temperature signal to the main unit after batteries inserted.

- If main unit failed to receive transmission from outdoor thermo sensor in first 3 minutes after the batteries inserted (“- - . –”display on the LCD), hold “SEARCH” button (B4) for 2 seconds to receive transmission manually.

6.2 Outdoor Temperature Alert Function

- Press “ALERT” button (B2) to select to activate or deactivate outdoor temperature alert function.

- press ALERT button select to:

Active outdoor upper temperature alert, the icon “” besides outdoor temperature digit would display.

Active outdoor upper& lower temperature alert, the icon “” besides outdoor temperature digit would display.

Active outdoor lower temperature alert, the icon “” besides outdoor temperature digit would display.

Deactivate outdoor temperature alert, alert icon disappear.

- Hold “ALERT” button (B2) for 3 seconds to enter outdoor temperature alert setting. Icon “” or “” beside Temperature’s digits flash. Press “+” or “-“button to adjust the setting value, press “ALERT” button (B2) to confirm the setting. Setting Sequence as follow: Upper limit of temperature, Lower limit of Temperature.

- When it’s alert, the corresponding icon “” or “” would flash on the LCD. Press any buttons to stop the alert sound.

REMARK: if the temperature is out of the measurable range, LL.L (beyond the minimum temperature) or HH.H (beyond the maximum temperature) will be shown on the LCD.

7. Time and Alarm Setting

7.1 Radio Controlled Clock:

- After main unit finishes receiving the transmission from outdoor sensor, the clock automatically starts to scan the DCF time signal. Radio Control Icon“” flashes on the LCD.

| flashes， Indicating now is receiving DCF signal | turns on, Indicating signal received successfully | disappear, Indicating signal reception failed |
| --- | --- | --- |

- The clock automatically scans the time signal at 3.00 a.m. every day to maintain accurate timing. If reception fail, scanning stops (“” on LCD disappear) and repeats again at 4.00 a.m. and 5.00a.m.

- The clock can be set to scan the time signal manually by holding “+”& “-“buttons (B5&B7) for 2 seconds. Each reception takes about several minutes. If receptions fail, scanning stops. (“” on LCD disappear)

- Stop scanning by holding “+”& “-“buttons (B5&B7) for 2 seconds

- “” shown on the LCD means it is in Daylight Saving Time Mode.

7.2 Manual Time Setting:

- Hold “MODE” button (B4) for 3seconds to enter settings.

- Press “+” or “-” button (B5&B7) to change setting. Press “MODE” (B4) to confirm and move to the next setting.

- The setting options are as follows: RCC ON/OFF, Time Zone, 12/24 Hour, Hour, Min, Second, Year, Month, Date, Weekday Language and C/F.

- 8 languages can be selected in Day-of-week, they are: German, French, Spanish, Italian, Dutch, Denmark, Russian, and English.

- The languages and their selected abbreviations for each day of the week are shown in the following table.

| Language | Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday |
| --- | --- | --- | --- | --- | --- | --- | --- |
| German, GE | SO | MO | DI | MI | DO | FR | SA |
| English, EN | SU | MO | TU | WE | TH | FR | SA |
| Russian, RU | BC | ПН | BT | CP | ЧТ | ПТ | СБ |
| Denmark, DA | SO | MA | TI | ON | TO | FR | LO |
| Dutch, NE | ZO | MA | DI | WO | DO | VR | ZA |
| Italian, IT | DO | LU | MA | ME | GI | VE | SA |
| Spanish, ES | DO | LU | MA | MI | JU | VI | SA |
| French, FR | DI | LU | MA | ME | JE | VE | SA |

Note:

- Second adjusted to zero only.

- The Time Setting Mode will automatically exit in around 15 seconds without any adjustment.

- For Time Zone: If you receive no RC-DCF frequency signal, the time zone should be set to 0. Time Zone is used in countries which can received the DCF frequency signal but the time zone is different from German Time ( i.e. GMT+1).

7.3 Dual Daily Alarm Setting:

- Press “ALARM” button (B8) select to set the Alarm Time 1 & Alarm Time 2. Alarm time digit flashes, press “+” or “-” button to change setting, and press “ALARM” button (B8) to confirm and move to next setting.

7.4 Snooze Alarm Function:

- Press “ALARM 1” or “ALARM 2” button (B3 or B9) select to activate or deactivate alarm 1 or 2 function.

When it is on, the alarm time and alarm symbol (““or ““) display on the LCD.

- When alarm alerts, the corresponded icon “” or “” flashes, except “SNOOZE” button, press any buttons to stop the alarm. Otherwise, the alarm signal sounds for about 2 minutes, then stops automatically.

- Press “SNOOZE” button when alarm alerts, snooze icon “” flashes, the alarm snoozes for around 5 minutes, and then it alerts again. The snooze function can be enabled for maximum 7 times.

8. Projection:

- Press “PROJECTION” button to turn on or off projection function.

- When projection function is on, hold “PROJECTION” button for 2 seconds to reverse the projection content 180°.

9. Backlight

Hold “DIMMER” button (B1) around 2 seconds to select the brighter or darker display or turn off backlight.

10.  Low battery indication:

The low battery icon “”will appear, indicating that thermo sensor is in low battery status. The batteries should be replaced.

11. Precautions

- Use a pin to press the reset button (B6) if the Unit does not work properly.

- Avoid placing the clock near interference sources/metal frames such as computer or TV sets.

- The clock loses its time information when the battery is removed.

- Do not expose it to direct sunlight, heavy heat, cold, high humidity or wet areas

- The outdoor sensor must not be set up and installed under water. Set it up in away direct sunlight and Rain

- Never clean the device using abrasive or corrosive materials or products. Abrasive cleaning agents may scratch plastic parts and corrode electronic circuits

# Text boxes

Market supplier:

Jasněna Vláhová

Nové Město nad Metují

www.vlahova.cz