KW9230TH

USER MANUAL

- Features

1.1	Temperature              -   Indoor measurable range: -10°C ~+ 50°C

-   Past 24 Hrs Maximum & Minimum

Temperature record

1.2	Humidity                 -   Indoor measurable range: 20% ~ 99%

-   Past 24 Hrs Maximum & Minimum

Humidity record

1.3 Comfort Icon             -   Comfort Icon according to temperature and humidity

2. Main Unit Appearance

2.1 Part A- LCD

A1: Past 24 hrs Minimum & Maximum Temperature Record

A2: Temperature

A3: Comfort Indicator

A4: Humidity

A5: Past 24 hrs Minimum & Maximum Humidity Record

2.2 Part B- Buttons

B1: “C/F” button

B2: “▲” button

B3: “▼” button

B4: “ALERT” button

B5: ”RESET” button

2.3 Part C- Structure

C1: Wall Mount Hole                   C2: Battery Compartment

C3: Stand

3. Getting Started:

- Open battery Cover

- Insert 2 x AAA size batteries observing polarity [“ +” and “ –“ marks]

- Replace battery compartment cover

- Wall mounted by the hanging hole (C1), OR place the unit onto flat surface, the unit is ready for use now.

4. Temperature & Humidity5

4.1 Temperature& Humidity

- After start-up, the unit would display indoor Temperature, Indoor humidity and Past 24 Hours Indoor Maximum and Minimum Temperature and Humidity Record.

4.2 Celsius / Fahrenheit

- Press “°C /°F” button (B1) to select Indoor Temperature in Celsius mode or Fahrenheit mode.

- If the temperature is out of the measurable range, LL.L (beyond the minimum temperature) or HH.H (beyond the maximum temperature) will be shown on the LCD.

4.3 Comfort Indicator Icon

There are four different icons would be display according to the temperature and humidity condition:

4.4 Temperature & Humidity Alert function:

- Press “ALERT” button to select to activate the alert function for this channel. Once ALERT function is activated, the icon “” appears on the LCD.

Ppress ALERT button select to:

- Hold “ALERT” button for 3 seconds to enter Temperature & Humidity Alert setting. Icon “” beside Temperature’s digits flash.

- Press “▲” (B2) or “▼“ (B3) button to adjust the value, and press “ALERT” button to confirm each setting.

- Setting Sequence as follow: Upper limit of temperature, Lower limit of Temperature, Upper limit of Humidity, Lower limit of Humidity.

- When it’s alert, the corresponding icon “” or “” would flash on the LCD. Press any buttons to stop the alert sound, otherwise, it will sound for 2 minutes, and stop automatically.

Note: The Setting Mode will automatically exit in 15 seconds without any adjustment.

REMARK:

If the unit shows values that are obviously incorrect, you can reset it the unit.

Take a pointed object, and insert it into the RESET (B5) opening. The unit is reset and all record including past 24 hours max/min temperature and humidity would be clear.

5. Precautions

- The unit loses its information when the battery is removed.

- Do not expose it to direct sunlight, heavy heat, cold, high humidity or wet areas

- Never clean the device using abrasive or corrosive materials or products. Abrasive cleaning agents may scratch plastic parts and corrode electronic circuits

6. Specifications

| Unit Dimensions: | 104 x 72 x 18.5mm |
| --- | --- |
| Battery Requirements: | 2 x AAA batteries |
| Humidity Range | 20% to 99% |
| Temperature range: | -10°C to +50°C |